## Slide 1
Lecture ten

## Slide 2: A* algorithm
It is an advanced BFS algorithm that searches for shorter paths first rather than the longer paths. A* is optimal as well as a complete algorithm.
Optimal meaning that A* is sure to find the least cost from the source to the destination and Complete meaning that it is going to find all the paths that are available to us from the source to the destination.
in most cases A* the best algorithm. But A* is slow and also the space it requires is a lot as it saves all the possible paths that are available to us. This makes other faster algorithms have an upper hand over A* but it is nevertheless, one of the best algorithms out there.

## Slide 3: A* Algorithm:
Add start node to list
For all the neighbouring nodes, find the least cost F node
Switch to the closed list
  For 8 nodes adjacent to the current node
  If the node is not reachable, ignore it. Else
    If the node is not on the open list, move it to the open list and calculate f, g, h.
    If the node is on the open list, check if the path it offers is less than the current path and change to it if it does so.
Stop working when
  You find the destination
  You cannot find the destination going through all possible points

## Slide 4
Heuristic Function Is a function that maps from problem state descriptions to measures of desirability, usually represented as numbers.
The function F can be constructed as the sum of two terms:
f(n) = g(n) + h(n)
where g(n) measures the actual length of the path from any state n to the start state, and,
h(n) is the heuristic estimate of the distance from state n to a goal.

## Slide 5
A* algorithm

## Slide 6
Node n | Heuristic function h(n)
A | 40
B | 28
C | 30
D | 34
E | 73
F | 86
G | 30
H | 37
I | 35
J | 37
K | 31

## Slide 7
Iteration | Node | OPEN | CLOSED
0 |  | [A40] | [ ]
1 | A40 | [B28 C30 D34] | [A]
2 | B28 | [C30 D34 E73 F86] | [A40 B28]
3 | C30 | [D34 E73 F86 G30 H43 I35] | [A40 B28 C30]
4 | G30 | [D34 E73 F86 H37 I35] | [A40 B28 C30 G30]
5 | D34 | [E73 F86 H37 I32] | [A40 B28 C30 G30 D34]
6 | I32 | [E73 F86 H37] | [A40 B28 C30 G30 D34 I32]
7 | H37 | [E73 F86 J46 K31] | [A40 B28 C30 G30 D34 I32 H37]
8 | K31 | [E73 F86 J46] | [A40 B28 C30 G30 D34 I32 H37 K31]
PATH solution: A C  G  H  K.